# Residential Information Handout

GENERAL INFORMATION	2

Public Works Department Information	2

Contacts	2

BUILDING CODE INFORMATION	3

Codes Used By Alleghany County	3

How To Get A Copy of the Current Codes	3

BUILDING PERMIT INFORMATION	4

When a Residential Building Permit is Required	4

General Permit Information and Who May Apply	4

General Permit Process For Residential Construction	5

Fees	5

Requirements for a Residential Building Permit	5

TYPES OF PERMITS REQUIRED	7

Electrical, Plumbing, and Mechanical Permits	7

INSPECTIONS	8

Building Inspections Required	8

Minimum Inspections Required	8

Footer Inspection	9

Residential Electrical Rough In	10

Residential Plumbing Rough In	11

Residential Mechanical Rough In	12

Framing Inspection	13

Final Inspection	14

## GENERAL INFORMATION

### Public Works Department Information

Office Hours:	8:00 AM – 5:00 PM Monday through Friday

Alleghany County Public Works Department encompasses both the Building Inspections and Zoning Offices.   Mailing address is as follows:

9212 Winterberry Avenue, Suite A

Covington, VA  24426

Phone:  540-863-6650

Fax:  540-863-6655

www.co.alleghany.va.us

### Contacts

Chuck Little, CBO	Building Official/Building Inspector

Andy Morris	Building Inspector / E & S Administrator

Shelly Dudley 	County Planner/Zoning Administrator

#### Power Companies

| BARC 100 High Street PO Box 264 Millboro, VA 24460 (800) 846-2272 | Craig Botetourt P.O. Box 265 New Castle, VA 24127 (540) 864-5121 | Dominion Virginia Power 2307 Beech Avenue Buena Vista, VA 24416 (888) 667-3000 |
| --- | --- | --- |

#### Virginia Department of Transportation Offices

| Covington Headquarters Grayson Avenue Covington, VA 24426 (540) 962-4206 | Lexington Residency PO Box 934 Lexington, VA 24450 (540) 962-8913 or (540) 463-3108 |
| --- | --- |

#### Other

| Alleghany-Covington Health Department 321 Beech Street P.O. Box 747 Covington, VA 24426 (540) 962-2173 | Miss Utility (800) 552-7001 (800) 552-3120 (for ticket status) |
| --- | --- |

## BUILDING CODE INFORMATION

### Codes Used By Alleghany County

For residential construction, Alleghany County is using 2003 Virginia Uniform Building Code (VUSBC), which went into effect on November 16, 2005.  The VUSBC references the 2003 International Residential Code (IRC) as the official residential building code for Virginia. In turn the 2003 IRC references the 2002 National Electric Code (NEC) for all electrical issues.

SEVERAL POINTS SHOULD BE NOTED:

- These codes are the minimum allowable standards, and the homeowner or contractor may build to higher performance standards.

- While all municipalities abide by the same codes, the requirements for one jurisdiction may be different from those requirements in another municipality (example: the wind conditions at the beach are different than here in Alleghany County, and should therefore mandate different wall bracing).

### How To Get A Copy of the Current Codes

A copy of the residential portion of the VUSBC is called the 2003 Virginia Construction Code and it can be downloaded from the Virginia Department of Housing and Community Development web page at:

http://www.dhcd.gov/StateBuildingCodesandregulations/PDF’s/Virginia Construction Code USBCPart 1.pdf

The 2003 International Residential Code can be purchased from The International Code Council by phone at (888)786-4452 or go to ICCSAFE.org.  Please note that there are other more current years of the IRC available, so be sure to specify the 2003 edition.   Codes can also be viewed at the Public Works Department.

## BUILDING PERMIT INFORMATION

### When a Residential Building Permit is Required

Building permits are issued for the construction of new residential dwelling, addition or alterations to existing residential structures.  Certain routine minor repairs are exempt and may include the following:

- Repair of porch floors or steps of like material and dimensions

- Roof repair or replacement of shingles on existing residential buildings

- Detached structures such as garages or storage building that measure less than 150 square feet

- Replacement of existing windows or doors

- Installation of siding

All new construction permits are required to have zoning approved by the Zoning Administrator.  Permits for new construction in the Town of Clifton Forge and the Town of Iron Gate will require a letter of zoning approval from the Town’s Zoning Official.  Each Town handles zoning individually.

Bona Fide farm buildings and structures not used for residential purposes, on property taxed as a farm, are exempt from the building code requirements except for flood plain requirements.

The building project must be started within six (6) months of issuing the building permit and timely inspections must be requested and approved by this office.  If the project is abandoned for six (6) months or more, the building permit is void and must be reapplied for at the Building Inspections Office.

### General Permit Information and Who May Apply

The current property owner or the designated agent may apply for the building permit.  However if the property owner has made arrangements with a contractor to perform the work note d in the permit application, it is strongly suggested that the contractor be the party to secure the permit.  The applicant securing the permit will be the party held responsible for the work being done in compliance with the applicable codes.  Applicants can file their completed application forms at the Building Inspections Office, Monday through Friday, between the hours of 8:00 AM and 5:00 PM.

Persons or firms, other than the owner, performing any work note don the permit application must be a Virginia licensed contractor under the regulations as set forth in the Department of Professional and Occupational Regulations (www.dpor.virginia.gov).

### General Permit Process For Residential Construction

The basic process for the construction of a new house (similar for additions, garages, decks etc.) is as follows:

- The Homeowner or Contractor prepares the construction documents.  For large or unordinary projects, it is advised to meet with the Building Official and discuss your project before you file your application.

- The completed application, construction documents and other required information are submitted to the County for review.

- The application is reviewed for completeness and the plans are reviewed for structural integrity and code compliance.

- Your application and plans are approved and a building permit is issued.

- Construction begins.

- Inspections are made periodically throughout the construction process.

- A Certificate of Occupancy is issued after house is complete and prior to occupying the dwelling.

### Fees

All building, electrical, plumbing, and mechanical permit fees are based on the estimate cost of the work and should include the reasonable value for labor and material regardless of who does the work, owner or contractor.  Checks should be made payable to the Alleghany County Treasurer.  A copy of the fee schedule is available upon request from the building department or can be viewed on the county web page.

### Requirements for a Residential Building Permit

Applicants must file a completed building and zoning permit application with the required attachments, with the Public Works Department for review and approval by the Building Official and Zoning Administrator, and other departments were necessary.  The application can be obtained from the Public Works Department and the following general information is required on the application.

Current property owner’s name, mailing address and telephone number. If the property has been owned for less than one year, a copy of the present owner’s recorded deed will be required.

Name, mailing address, telephone number, state registration card number, expiration date and classification of the contractor is required.

Two (2) sets of plans along with the 16-item Plans Review Checklist must be submitted for a single-family dwelling. Wind and snow load must also be stated on the plans. Normal review time is 1-2 working days.  Snow Load:  30 psf (per square foot)   Wind:  90 mph, 3 second gusts.

Accurate directions to the construction site will be needed.  Please be sure to use the street names and/or route numbers for accuracy.

General information needed for a building permit application may include: type of wall construction, heating source, water/sewer source, dimensions of building project, number of bedrooms, number of bathrooms, number of stories, square footage, building height, etc.

Lot, block and section number of parcel is needed if the property is located within a subdivision.

Water and sewer:

*Private system – Approved well and septic construction permits from the 
Health Department are required at the time of application;

*Public system -- A copy of the water and wastewater application or paid connection receipt from Alleghany County Public Works is required at the time of application.

A site plan is required and shall show at a minimum the following:  property boundary lines, location of existing and proposed structures, proposed alteration or addition; streets, road, driveways or right-of-ways; utility easements; location of creeks, rivers or streams; the distance the existing and proposed structures are from property lines, streets, roads, right-of-ways or easements.

If your driveway will enter onto a state maintained road, a copy of the “Driveway Entrance Permit” will be required at the time of application.  Office locations for the Virginia Department of Transportation are found on our information sheet.

An Erosion and Sediment Control “Agreement in Lieu of “ form must be signed by the owner/contractor for each dwelling.

## TYPES OF PERMITS REQUIRED

### Electrical, Plumbing, and Mechanical Permits

Electrical, plumbing, and mechanical are included with the permit for a new single-family dwelling, however permits maybe issued separately if the applicant requests it.  If separate permits are to be requested, applications for each permit type will need to be filed with the building department after the dwelling permit has been issued.  Applications may be obtained in at the building department, by mail or on the County web page.

For electrical, plumbing or mechanical work being done on existing residential structures applications for each permit type will need to be filed with the building department after the dwelling permit has been issued.  Applications may be obtained in at the building department, by mail or on the County web page

Electrical services such as Temporary Pole, Upgrade of Service, or New Permanent Service should be applied for with the power company servicing your area as soon as the need is known.  Three electric companies serve the Alleghany County Area, and are listed in the General Information section of this booklet.

note:  Mechanical permits are required when any type of fuel gas is installed or replaced.

## INSPECTIONS

### Building Inspections Required

The building permit shall be posted on the site so as to be visible from the entrance of the property or street and should be protected from the weather.

A complete set of approved plans shall be on the job site for the inspector’s review on all inspections.  If any changes and/or additions to the plans are made after the permit is issued, you are required to submit a set of revised plans to the building official for approval.

The contractor/permit holder doing the actual work shall call in all inspections, and the work must be ready for inspection at the time of request.  When calling in the inspection request, please have the following information ready:  permit number, applicant name, street address, and type of inspection needed.

Inspections called in during office hours (8:00 AM to 5:00 PM) are done the following business day. Same day inspections are not done unless time allows, except for footings and they must be called in by 7:30 AM.

If the requested inspection is not ready when the inspector arrives on the job site, the inspection will be rejected and a re-inspection will be required.   All re-inspection fees will be required to be paid to the building office after final inspection and prior to the Certificate of Occupancy or any other permits being issued.

### Minimum Inspections Required

The Virginia Uniform Statewide Building Code (USBC), Volume I, requires that the following minimum inspections be conducted when applicable to the construction or permit:

- Footing

- Rough-In Electrical

- Rough-In Plumbing

- Rough-In Mechanical

- Rough-In Framing

- Final Inspection

A list of required building inspections follows. The items listed for each specific inspection are to be considered a guideline, and may or may not apply to all residential construction.

### Footer Inspection

Construction entrance and erosion & sediment control devices shall be in place before footing inspection.

Footers are to be dug straight.

Bottoms are to be level and a minimum of 18” below finished grade.

Bulkheads are to be in place not less than 12” from step-downs.

Pier footings are to be dug to size and depth as shown on approved plans.

All mud, soft areas, loose dirt, water and roots are to be removed before inspection.

Reinforcing steel (re-bars), where required, installed in accordance with the International Residential Code and the American Concrete Institute. Grade markers must also be in place.

note: No footer inspections will be made until the building permit application is approved and the permit issued to the applicant. Do not order concrete for footers until footer has passed inspection.

### Residential Electrical Rough In

All wiring and boxes installed for smoke detectors

All wiring and boxes installed for switches and receptacles

Disposal wiring

Water heater

Washer and dryer outlets

Lighting for each exit door

Stair lighting wired for 3-way switch

Counter-top receptacles

Exterior receptacles

Light and receptacles for attics and crawl spaces

Fan boxes if needed

All metal boxes grounded

note: All switches and receptacles are to be made ready to receive device.

Power Only Permit – Homeowners or contractors may wish to install permanent power to the home prior to the structure being ready for a final occupancy inspection. The following must be complete before power only can be approved:

Permanent roof, meter base, service equipment and grounds shall be in place.

Access to panels shall be secured by either locking the electric panel or the building.

At least one GFCI receptacle must be installed. Any additional circuits that have been installed must be complete.

Conductor shall be installed for grounding or bonding water line.

### Residential Plumbing Rough In

Drain, Waste and Vent (DWV)

All groundwork installed, tested and inspected prior to basement slab being poured.

All DWV installed to all fixtures, washing machines, tubs, showers, toilets, and sinks.

All DWV tested by either filling system with water and creating a minimum 10’ of head or by testing with air at 5 psi.

All clean outs must be installed at rough in.

For connection to a public sewer system, will be performed by Alleghany County Public Works personnel when the connection fees have been paid and the building is ready to be connected to the public sewer.

Water

All waterlines completed and installed to all fixtures, washing machines, water heater, tubs, shower, toilets, and sinks.

Waterlines are to have all required valves installed, except for sink and toilet supplies.

No PVC water piping is to be used.

Waterlines are to be tested at the time of inspection at 50 psi or more.

All plumbing, DWV and water, are to be buried at a minimum depth of 18” once the lines have been taken outside of the perimeter of the structure.

### Residential Mechanical Rough In

All heating and air conditioning equipment that will become concealed must be installed and in some cases, hydronic piping, gas lines, etc. will require testing.

Holes must be cut for registers in floors and/or ceilings.

Refrigerant lines must be insulated and run from air handling units to heat pump locations.

All exhaust ducts to be installed (bathroom, dryers, and kitchen)

All chimneys and flues to be installed

Condensate drains in attic units must be complete.

Pan and the pan drain, or a water level detection device or switch must be installed in attic units.

All supply ducts must be installed.

Return air ducts must be installed.

A gas line test must be not less than 3 psig.

The hydronic pipe shall be tested at 100 psi minimum.

### Framing Inspection

*** note: No insulation is to be installed before the framing inspection is approved.

“All utilities” must be roughed in and inspected (plumbing, electrical and mechanical) before calling for a framing inspection.

Manufactured fireplace and chimney inserts shall be installed.

Fire blocking up stair walls and between joists over bearing walls shall be in place.

Firestopping around pipes, wires and ducts through both top and bottom plates of stud walls and chases shall be in place using fire-rated sealant.

All structural members, their spans and attachments (nailing, joist hangers) are to be in accordance with code and as shown on approved drawings.

Wood sills that rest on concrete or masonry walls shall be pressure treated.

Sub flooring shall be nailed in accordance with code.

All attic areas are to be vented in accordance with code.

Attic access must be framed in.

Stairs are to be installed, check tread risers and head clearance for code compliance.

All windows and doors must be installed.

### Final Inspection

Copy of Well and Septic Operations Permit (if applicable).

Have insulation certification signed and on site at/or before requesting final inspection, or have a detailed receipt from insulation contractor available (may include fire-stopping).

Paper vapor barriers or insulation shall not be left exposed (flammable).

Handrails down steps must be installed where there are 4 or more risers.  Top of rail is to be 34 to 38 inches above tread nosing.

Guardrails at porches, balconies or raised floor surfaces located more then 30” above the floor or grade, are to be no less than 36” above floor.  Intermediate rails shall not have more than 4” open space between them.  Stairway guardrails are to be no less than 34” above tread nosing.

Check fireplace size, damper, hearth extension, combustion air and clearance of wood trim from fireplace opening.  (See Code).

Check to see that yard grade drains away from the house.

Each structure to which a street number has been assigned shall have the number displayed so as to be readable from the public right of way.

Seal all penetrations thru exterior sheeting, foundation, etc.

Paint all exposed steel piping on gas lines.

All light fixtures in place.

All required plumbing fixtures in place.

Paint all metal railings, lintels, etc.

Protect all exposed untreated wood.

All Final Inspections are to be completed
 before the owner is allowed to occupy the structure.